## Slide 1
01
AI MELT-SHOP INTELLIGENCE
METALLISENSE
Catch raw-material problems at the gate, not in the furnace — then correct every heat with explainable, self-improving AI.
Pre-Melt Gate · Deviation Analysis · Correction Planner · Adaptive Strategy Optimizer

## Slide 2
WHY THIS MATTERS
Defects are found after the metal is melted
02
After
MELTING
A bad charge shows up only at the first spectrometer reading — energy, time and metal are already spent.
0%
REFINING
An induction furnace cannot remove excess Cu, Cr, P or S. Only a different charge fixes it.
₹21,000
PER TONNE
Lost when an SG-iron heat is downgraded to grey iron (illustrative selling prices).

## Slide 3
THE SOLUTION
One heat, one flow: from truck to tap
03
Raw Material Stock
Lots + ledger
›
Yard Inspection
XRF / LIBS gun
›
DRI QA Lab
Maker–checker
›
Pre-Melt Gate
GO / WARN / HOLD
›
3 AI stages
Deviation → Correction → Strategy
›
Tap approval
Mechanical properties
Each stage unlocks the next. The gate's predicted melt-down chemistry flows automatically into the AI stages — no retyping, no synthetic data.

## Slide 4
04

## Slide 5
RAW MATERIAL · YARD INSPECTION
Every lot is trusted before it is charged
05
Chemistry trust (1σ)
Supplier declared
15%
Mill certificate
6%
QA lab (approved)
3%
Parent heat OES
3%
Handheld gun
Flags only
Gun decision (400-piece hidden load)
Any stainless piece, ≥ 20% alloy or ≥ 10% copper → QUARANTINED
Some copper or alloy pieces → RESTRICTED (max 20–25% of charge)
< 70% reliable readings (paint, oil, rust) → clean and re-test
Nothing flagged → RELEASED

## Slide 6
DRI QA LAB
Sponge iron needs a second signature
06
Lab entry
Fe total, Fe metallic, C, P, S (+ gangue, moisture, fines)
Validation
Hard limits reject; unusual values need confirmation
Second approver
Same person as analyst → refused (403)
Release rules
Rule | Release | Restrict | Quarantine
Metallization | ≥ 85% | 80–85% (25%) | < 80%
Phosphorus | ≤ 0.05% | ≤ 0.08% (25%) | > 0.08%
Sulphur | ≤ 0.03% | ≤ 0.05% (30%) | > 0.05%
Metallization = Fe metallic ÷ Fe total. Moisture > 1% or a result older than 7 days raises a gate warning.

## Slide 7
FURNACE INTERLOCK
Pre-Melt Gate: 8 checks, one decision
07
1
Charge weight
2
Lot release status
3
Stock available
4
Handheld XRF / LIBS
5
Sponge-iron lab
6
Predicted chemistry vs grade
7
Residuals Cu Cr Ni Mo Sn
8
AI off-spec risk
GO
All pass — furnace may start
WARN
Operator must tick the warnings
HOLD
Locked — engineer override + written reason

## Slide 8
MELT-DOWN CHEMISTRY · AI RISK
Predicting the melt before it exists
08
Charge → bath chemistry
Metal weight: kg × yield (scrap 95%, pig iron 97%, returns 98%; DRI from its lab result)
Bath value: metal-weighted average × melt recovery (C 96%, Si 95%, Mn 93%)
Uncertainty: each lot's trust level combined + 2% process variation
Fe is the balance; each element traced to the lot it came from
0.95–0.97
holdout AUC, per grade
400
Monte-Carlo samples inside σ
2 passes
risk before and after additions
Notes: Model: HistGradientBoostingClassifier, one per grade, features C Si Mn P S, trained on is_deviated labels in dataset.csv. If risk stays >= 50% after the Melt Correction Planner's additions, the gate holds: the charge must change.

## Slide 9
AI STAGE 1
Composition Deviation Analysis
09
Isolation Forest
200 trees, contamination 0.35, trained on 200,000 heats
18 features: 6 elements + deviation from spec midpoint + out-of-range flag per element
Short isolation path = abnormal; score rescaled to 0–1
Result unlocks the Melt Correction Planner
Severity
LOW
0.00 – 0.33
MEDIUM
0.33 – 0.66
HIGH
0.66 – 1.00

## Slide 10
AI STAGE 2
Melt Correction Planner
10
Multi-output gradient boosting
Target: gap to grade midpoint, additions only
One regressor per element (100 trees, depth 5)
Caps: 5% per element; in-spec heats get no additions
Too-high elements → dilution warning
Additions converted to kg of in-stock FeSi-75, HC FeMn, recarburiser (FIFO)
Chart: Confidence score weights (%)
| Addition size | No. of corrections | Total deviation
Confidence | 40 | 30 | 30

## Slide 11
AI STAGE 3 · ONLINE REINFORCEMENT LEARNING
Adaptive Strategy Optimizer
11
0.3×
Conservative
Smallest additions, lowest overshoot risk
1.0×
Balanced
Full model correction, best trade-off
2.0×
Aggressive
Over-corrects, fastest pull into spec
Learned reward model
SGD regressor scores each (deviation, grade, additions) pair and is updated after every operator decision — no retraining pipeline.
Reward = outcome bonus + measured improvement − 0.05 × weighted cost
Accepted +0.4 · Modified 0 · Rejected −0.6
Safety clip: C, Si ≤ 1.5%, Mn ≤ 1.0%, total ≤ 6%

## Slide 12
STRATEGY COMPARISON
Choosing a strategy: the composite score
12
Chart: Composite weights (%)
| Added CO₂ | Spec compliance | Correction cost | Predicted reward
Weight | 15 | 25 | 25 | 35
How it works
Each metric normalised across the 3 strategies (best = 1)
Mechanical FAIL costs 0.5 on spec compliance
−10 points per constraint violation
Grid marks the best per metric and 'Best overall'
Accept one → the other two lock; stock is deducted

## Slide 13
COST · CARBON · PROPERTIES
Every strategy priced, weighed and tested
13
Cost
Base metal ₹/kg × batch + element kg × alloy price + strategy premium (₹800 / 4,300 / 11,300)
Carbon
Base factor × batch + element kg × CO₂ factor (FeSi 4.0, FeMn 2.8 kg CO₂e/kg)
Savings
Downgrade loss per tonne − correction cost; shown as % of selling price
Mechanical
UTS, YS, elongation, HB from C Si Mn P S, checked against IS 2062, 1570, 210, 1865

## Slide 14
COPILOT · VOICE
Explainable, hands-free AI
14
Explainable copilot
Groq LLM (switchable to Claude or Gemini) turns every result into plain-language reasoning and operator guidance.
Voice questions
Groq Whisper large-v3 transcribes the operator's spoken question.
Read aloud
ElevenLabs multilingual voice reads the gate decision and strategy comparison; gTTS and browser voice as fallbacks.
Semantic memory
Similar past heats found by meaning, via vector search.

## Slide 15
TECH STACK
Built on five independent services
15
Service | Port | Stack | Role
Frontend | 5173 | React 18, Vite, Tailwind, Recharts | All screens
Backend | 3000 | Node.js, Express, node-opcua | API, gate engine, cost, orchestration
AI service | 8000 | FastAPI, scikit-learn | Deviation + correction models
Agent service | 8001 | FastAPI, Groq, ElevenLabs | RL, risk model, copilot, voice
Vector search | 8002 | Actian VectorAI / NumPy | Semantic search
OPC UA | 4334 · 4335 | node-opcua | Spectrometer + gun simulators

## Slide 16
ROADMAP
Honest limits and what comes next
16
Limits today
Models trained on synthetic data; prices and limits illustrative
Gun samples pieces and can miss one — spectrometer check stays
Real guns export CSV/Bluetooth; simulator uses OPC UA
State in memory; restart resets
Next
Re-run the gate on every mid-melt addition
Weigh actual charged kg at the bucket
Learn from gate vs spectrometer error
Persist to a database; plant-specific limits

## Slide 17
17
Caught at the gate —
not in the furnace.
MetalliSense · AI melt-shop intelligence